## Slide 1
AVR EMBEDDED SYSTEMS
REAL-TIME CLOCK & TIMING UNIT
A compact embedded platform for clock, calendar, alarms and timing control.
14 : 12 : 12
RTC • AVR
Graduation Project | ATmega32 | I2C / TWI

## Slide 2
01 • TEAM
Project Team
Prepared and developed as an AVR embedded-systems graduation project.
Adel Wael Adel
Yousef Mahmoud Elsayed
Abdullah Mohammed Abdullah
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
02

## Slide 3
02 • PURPOSE
Project Overview
01
What we built
A multi-function real-time clock centered on an ATmega32, with
an LCD interface and push-button control.
02
Four timing modes
Clock & calendar, programmable alarm, stopwatch,
and countdown timer.
03
Core hardware
ATmega32 + RTC module + 16×2 LCD + push buttons + buzzer.
04
Design approach
Separate hardware drivers from application logic through
a layered embedded-software structure.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
03

## Slide 4
03 • PROJECT CHOICE
Why This Project?
01
Useful in practice
Time-dependent control appears in consumer devices
, industrial systems and automation.
02
More than a clock
The design combines four useful timing functions rather
than stopping at basic time display.
03
Full-stack embedded work
The project brings together peripherals, communication,
firmware and a user interface.
04
Ready to extend
The same architecture can support reminders, scheduling and
automated device control.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
04

## Slide 5
04 • SYSTEM HARDWARE
Hardware Building Blocks
01
ATmega32
Main controller responsible for application flow, input handling,
timing and peripheral coordination.
02
RTC module
DS1307 / DS3231 family used to retain current time and calendar
information through I2C/TWI.
03
16×2 character LCD
Provides continuous feedback for time, date, operating mode and
timer values.
04
Push buttons + buzzer
Buttons handle navigation and adjustments; the buzzer supplies
audible notifications.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
05

## Slide 6
05 • HOW THE PARTS CONNECT
System Architecture
01
RTC → ATmega32
The RTC supplies real-time and calendar data over the two-wire
I2C/TWI interface.
02
ATmega32 → LCD
The controller formats the current state and presents it on the
16×2 display.
03
Buttons → ATmega32
User actions select modes and change settings such as time,
date and alarm values.
04
ATmega32 → Buzzer
The controller triggers audible feedback when an alarm or
countdown reaches its target.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
06

## Slide 7
06 • MAIN FEATURES
Functional Modes
01
Clock & calendar
Shows hours, minutes, seconds and full date, with manual
adjustment available.
02
Programmable alarm
User sets an alarm target, enables it, and receives a buzzer
notification when the time matches.
03
Stopwatch
Independent count-up measurement with start, pause/stop
and reset controls.
04
Countdown
User defines a duration; the remaining time updates live and
the buzzer sounds at zero.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
07

## Slide 8
07 • MODE 01
Clock & Calendar
The clock mode is the foundation: the RTC provides the reference while the MCU handles presentation and user adjustment.
01
Continuous timekeeping
The RTC maintains current time and date independently of the
main application loop.
02
Display format
Time is shown as HH : MM : SS; the calendar
uses DD / MM / YY.
03
Manual correction
The user can adjust clock and calendar values through the
push-button interface.
04
Communication
ATmega32 reads and writes RTC data through I2C/TWI.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
08

## Slide 9
08 • MODE 02
Alarm Workflow
01
Set target
Choose the desired alarm hour, minute and related settings.
02
Enable
Turn the alarm function on; its state remains visible on the LCD.
03
Monitor
The application continuously checks the RTC against the
configured target.
04
Alert & silence
When the values match, the buzzer sounds and the user can
acknowledge the notification.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
09

## Slide 10
09 • MODE 03
Stopwatch Operation
01
Start
Begin elapsed-time measurement from the current zero state.
02
Pause / stop
Freeze the displayed value whenever the measurement needs
to be interrupted.
03
Reset
Return the stopwatch to 00 : 00 : 00.
04
Live display
The LCD provides continuous feedback while elapsed time
is being measured.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
10

## Slide 11
10 • MODE 04
Countdown Timer
01
Choose duration
Adjust hours, minutes and seconds before starting.
02
Run / pause
Start the countdown and pause it when required.
03
Track remaining time
The LCD updates the remaining duration in real time.
04
Finish alert
At 00:00:00 the buzzer notifies the user that the interval has ended.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
11

## Slide 12
11 • MCU ROLE
ATmega32: The Control Center
01
Application management
Runs the main program and selects the active operating mode.
02
Input handling
Reads push-button states and translates them into user commands.
03
Timing services
Uses hardware timers and periodic ticks for software timing operations.
04
Peripheral coordination
Controls communication with the LCD, RTC and buzzer.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
12

## Slide 13
12 • COMMUNICATION
RTC Communication via I2C / TWI
01
Two-wire link
SDA carries data while SCL provides the synchronization clock.
02
Master / slave flow
The ATmega32 acts as the controller and communicates
with the RTC device.
03
Calendar data
The exchange includes seconds, minutes, hours, day, month and year.
04
Why it fits
Only two signal lines are needed for reliable serial communication
with the RTC.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
13

## Slide 14
13 • INTERACTION
User Interface Flow
01
1 — Choose a mode
Move between Clock, Alarm, Stopwatch and Countdown using
the buttons.
02
2 — Edit values
Select the relevant time, date, alarm or duration field.
03
3 — Change values
Increase or decrease the selected value with dedicated controls.
04
4 — Confirm visually
The LCD immediately reflects the current state and user actions.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
14

## Slide 15
14 • SOFTWARE
Layered Firmware Design
01
MCAL
DIO, Timer, Global Interrupt and I2C/TWI drivers interface directly
with ATmega32 peripherals.
02
HAL
LCD, Keypad and RTC drivers hide hardware details and expose simpler
functions to the application.
03
Main application
Coordinates clock, alarm, stopwatch and countdown behavior.
04
Separation of concerns
Each layer depends on the one beneath it, making the code
easier to maintain and test.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
15

## Slide 16
15 • DRIVER LAYER
MCAL: Low-Level Drivers
01
DIO driver
Configures pins, reads button states, enables pull-ups and drives
outputs.
02
Timer driver
Uses CTC mode to generate periodic interrupts and a system
millisecond tick.
03
Global Interrupt driver
Enables or disables global interrupts safely for asynchronous events.
04
I2C / TWI driver
Provides the SDA/SCL communication path between the
ATmega32 and RTC.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
16

## Slide 17
16 • HIGH-LEVEL LOGIC
HAL + Application Layer
01
LCD driver
Initializes the display and sends commands, characters and strings.
02
RTC driver
Reads/writes time and date and handles Decimal ↔ BCD conversion.
03
Application modes
Coordinates Clock, Alarm, Stopwatch and Countdown functions.
04
Calendar logic
Includes the required date handling, including leap-year behavior.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
17

## Slide 18
17 • EXECUTION LOOP
Runtime Sequence
01
Power on
Initialize LCD, RTC, timer and all required I/O.
02
Read & show
Fetch current RTC information and refresh the LCD.
03
Process input
Read button states and determine the selected mode or
requested change.
04
Execute & repeat
Run the active mode, trigger the buzzer when required,
then continue the loop.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
18

## Slide 19
18 • PROTEUS
Simulation & Verification
Proteus was used as the integration environment before final hardware implementation.
01
RTC link
Check data exchange and I2C timing between the MCU and RTC.
02
LCD behavior
Confirm the displayed values and refresh behavior.
03
Button response
Validate button detection and debouncing behavior.
04
Timing + alerts
Verify alarm triggering, stopwatch/countdown behavior
and buzzer activation.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
19

## Slide 20
18.5 • PROTEUS
Simulation & Verification
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
20

## Slide 21
19 • REAL-WORLD USE
Broader Applications
01
Reminder products
Scheduled alerts for routine activities and important events.
02
Time-management tools
Meeting, study, exercise and cooking timers.
03
Home automation
Start or stop devices at predefined times.
04
Industrial control
Support time-dependent machine actions and process scheduling.
ADVANCED REAL-TIME CLOCK SYSTEM • AVR EMBEDDED PROJECT
21

## Slide 22
THANK YOU :)
Real-time clock • Alarm • Stopwatch • Countdown ATmega32 • RTC • LCD • I2C/TWI
Yousef Mahmoud Elsayed • Adel Wael Adel • Abdullah Mohammed Abdullah
2026 copyright @EDRA
Sufa, void and john was here